## Slide 1
Final Presentation
Machine Learning and Programming
Bogyeong Suh, Geon Kim, Sri Madhumitha Nelakanti, Tuli Barman
Project 8
Control Logic Synthesis for Manufacturing System using Meta Deep Reinforcement Learning

## Slide 2
1. Abstract
Background: Scheduling in manufacturing process is required for saving time and money. Especially for non-value adding tasks like Testing, an intelligent scheduling always becomes crucial.
Objective: Train deep reinforcement learning (DRL) algorithm to attain lower make-span for the entire process of testing the incoming products (pallets) than regular rule-based algorithms.
Methods: Deep Q-Networks with parallel training and customized reward function considering crowdness
Results: Our RL model showed 1,425 timesteps required to finish the procedure, beating the rule-based algorithms (1,548 and 1,546 timesteps for MIN and FCFS, respectively)
Conclusion: RL shows strength scheduling the crowdness of manufacturing process and can be used to shorten the overall make-span.

## Slide 3
2. Introduction
Manufacturing systems in factories
The testing process environment consists of 2 sections: A and B; each with 5 floors and 5 testers on each floor
Basically the incoming pallets are first to be 1) tested on a tester from Section A, 2) tested on a tester from Section B, and 3) they head to exit
The incoming rate of pallets is considered to be varying.
Testing time of all the testers follow a normal distribution.
Entrance
Exit
Section A
Section B
Lift
4th Floor
Tester A
Tester B

## Slide 4
3. Problem Statement
The incoming pallets are assigned to a tester A (in Section A), then to a tester B (in Section B), while ensuring least waiting time and crowding possible.
Constraint: Any chosen location in the environment (Tester, Conveyor belts, Lift area) can only accommodate up to maximum 1 pallet at any instant.
The crowded state
A pallet taking the lift
Crowded floor
The initial state
Entrance
Exit
Section A
Section B
Lift
4th Floor
Tester A
Tester B

## Slide 5
4. Methods
Deep Q Network (DQN)
-with Q Network and Target Q Network, learn action-value function minimizing DQN loss
Environment
DQN
reward
state
Action
Reinforcement Learning
States:
Status of all the testers and paths (occupied / idle)
Actions:
Floor selection (once each, for Section A and B)
Notes: Q Network: Approximate action-value function
Target Q Networks: Separate networks
Replay memory: Get random pieces from the stack of history(memory)

## Slide 6
4. Methods
Rewards:
1) When action is given to choose all-occupied floor,
2) When action is given to choose floor ,
case 1)
case 2) if : ,
if :
else:
3) When moving,
, , = weights

## Slide 7
4. Methods
Parallel training (concurrent training)
-while sharing the same environment, two different models train concurrently
Section A
Section B
Section A
Section B
Model 1
Model 2
Model 1: allocates pallets testing at section A
Model 2: allocates pallets testing at section B
Environment
Model 1
Model 2
Action
Action
Reward
Section A: all pallets start from entrance
Section B: pallets’ starting points are different

## Slide 8
5. Results
Performance results
Algorithms | Required timesteps
1. Rule-based algorithm: MIN | 1,548
2. Rule-based algorithm: FCFS | 1,546
3. RL with one model | 1,648
4. RL with two models (parallel training) | 1,597
5. RL with two models + customized reward function | 1,425
* MIN : Choose floors remaining the minimum number of pallets per floor
* FCFS: First-Come-First-Serve; Choose the lowest floor available (from the bottom to the top)

## Slide 9
5. Results
Our RL model vs Rule-based algorithms (MIN, FCFS)
Timesteps: 1,546
FCFS
Timesteps: 1,548
MIN
Timesteps: 1,425
RL model

## Slide 10
6. Discussion
RL model
Strength
-traffic jam due to lift resolved
-RL : tries to allocate pallets in section A to the same floor in section B
-MIN & FCFS : cannot allocate pallets to the same floor intentionally.  increased use of lift  waiting time↑
FCFS

## Slide 11
6. Discussion
Weakness
-less use of diverse floors
-RL : tries to use less number of floors
-MIN & FCFS : use all available floors if possible
FCFS
RL model
This can lead to wasted floors & increased time
Not used
All used

## Slide 12
6. Discussion
Limitation
1) Overgeneralized problem environment
    Testing times can be considered more specifically
    Speeds of motion of pallets can be considered
    Malfunction of testers (although state of such testers can be set to forever occupied until they start functioning normally again)
2) Limitation of our reward function
- less crowdness does not guarantee the minimum procedure time

## Slide 13
7. Conclusion
Contribution
-successfully trained a RL model recording lower tact time compared to the rule-based algorithms
-new reward functions considering crowdness
-parallel training of RL models
Future study
Improvement of reward function : terms relating required total procedure time
Consideration of 1) specific testing time, 2) speed of pallets, and 3) malfunction of testers